The battery Eater LED flasher circuit is made up of two identical circuits that each switch the other on and off.  Using the description below build the circuit and answer the questions.

Procedure:

1. Label the components with (+) and (-)

then bread board the circuit as shown:

2. Double-check all of your connections.

-Before connecting power have you circuit checked by the instructor. _______

3. Use a length of jumper wire (dashed line) connected to D-10 to touch the positive column.  What happens? ______________________________

4. Using the description on pages 216-217 of your text, describe what is happening to the transistor when you connect the jumper. _______________________________________

________________________________________________________________________________________________________________________________________________________________________________________________________________________

5. To finish the circuit, disconnect your battery and create a second circuit below the first, with jumpers connecting the two circuits. Use the diagram below to help you may want to add a (+) and (-) to each component to help when you are placing components.

When you are finished wiring, before the battery is connected have your instructor check your circuit.  ______________

# Text boxes

_____

_____

(Label Polarity)

Capacitor:

Transistor:	(Label legs with

correct names)